Anglicko-slovenský glosár železničnej terminológie

English-Slovak glossary of railway terminology

Zozbieral/Compiled by: 	Rastislav Geschwandtner

Použité zdroje/Sources: 	http://broadway.pennsyrr.com/Rail/Signal/glossary.html#trains

| English | Slovensky | Definícia/Definition |
| --- | --- | --- |
| [signal] mast | stožiar, stĺp | The vertical pole, usually round, on which the signal head(s) or arm(s) is/are mounted. |
| abutment | opora |  |
| arm | rameno | Each movable semaphore blade comprising a signal. In N. Am., analogously applied to lighted signals. Each arm provides a singular piece of information: 1 color, or 1 position, or 1 position and its attendant color. [Can anyone think of a case where the last sentence is NOT true?] Notably, 45 CFR ([U.S.] Code of Federal Regulations) seems to limit 'arm' to its literal meaning. |
| ballast | štrkové koľajové lôžko | The rocks (gravel) into which the track is set. |
| ballasted track | trať na štrkovom lôžku |  |
| board | rameno mechanického návestidla | British: slang for semaphore blade. N. Am.: slang, usually with an adjective ("clear board", "red board"). Probably stems from one method of displaying train order signals wherein a light was placed in front of a specific color board or flag. |
| bracket | konzola |  |
| bracket post |  | A pole supporting a platform, designed for the mounting of 2 or more signals (and their masts). |
| broad gauge | široký rozchod | Any gauge broader than Standard Gauge. In the U.S., predecessors of the Erie were built to a (?6-foot) broad gauge; the Russian (?5 foot) gauge is a "broad gauge" with respect to the worldwide "standard gauge". |
| capacity | priepustnosť |  |
| catenary equipment | trakčné vedenie |  |
| catch locking device | západkový uzáver výmeny |  |
| cess |  | British: the formation outside the ballast. |
| clamp locking device | čeľusťový uzáver |  |
| clamp locking device in modular tie | čeľusťový uzáver podvalový |  |
| classification yard | zoraďovacia stanica |  |
| clip | svorka alebo spona (podľa typu) | Where used, a "G" shaped piece of metal used to attaching the rail to the crosstie with a specific type of tie plate. In North America, the phrase "Pandrol clip", utilizing the manufacturer's name, is usually heard. |
| closing of a track to traffic | výluka trate |  |
| closure rail | skrátená (vyrovnávacia) koľaj | The non-mobile rail just beyond the point, between that and the frog. Most frequently, one is straight and one curved. |
| color-light signal |  | N. Am.: A signal that uses color to provide indications. As used by signalmen (signal engineers, signal maintainers, etc.) this term is used specifically to identify signal heads that have 1 lamp for each color (cf. 'searchlight'). As used by (at least some) books of rules, this term encompasses the term 'searchlight' (q.v.). British: 'Colour-light signal' includes searchlights, as does "multiple-aspect signal". |
| color-position-light signal |  | N. Am.: A signal that uses both color and position to redundantly provide indications. Only one color is associated with any given position, though this may vary according to the signal arm involved. Use was limited to Baltimore & Ohio (1920s to present) and Norfolk & Western (1950s to present), both now being removed, the latter a bit more quickly so. Amtrak has colorized former PRR signals, and these now qualify for the term 'CPL signal'. |
| crossing | koľajová križovatka | N. Am.: not related to switches. Refers to the structure allowing one track to cross over another. Britain: general term equivalent to N. Am. 'frog'. If the angle is acute, this is a 'common crossing'; if obtuse, an 'obtuse crossing'. Also 'crossing work'. |
| crossing | srdcovka | N. Am.: the piece of track that allows two tracks to cross over one another at grade. Also 'crossing diamond'. British: see under Switches. |
| crossing | kríženie | In America, a place where one track meets and crosses over the other without any connection. Each crossing has 4 frogs, and nowadays, is often prefabricated. |
| crossover | koľajová spojka | Two switches that allow a train to switch from one track to a parallel track. British usage also defines 'right hand' and 'left hand' with respect to the normal direction of travel on the left-hand track. |
| crosstie | pražec, podval | N. Am: The wooden cross-member that supports the rails. Crossties are less commonly made of concrete or steel, or sometimes absent, as when rails are set directly into concrete. |
| departure yard | odjazdová nákladná stanica |  |
| diamond crossing | križovatková výhybka, dvojitá srdcovka | British: equivalent to N. Am. 'crossing'. |
| diamond with double slip |  | British: equivalent to N. Am. 'double-slip switch'. |
| disc signal | terčové návestidlo |  |
| doll | trpasličie návestidlo | Britain: an arm carrying a signal blade that shorter than the main signal masts. |
| doll arm |  | N. Am.: a short subsidiary arm on a signal mast, bracket post, or signal bridge, usually with a light or reflectorized marker on it. The doll arm may be vertical only or may be horizontal, then vertical; the light or marker is most commonly blue or purple in color. A doll arm indicates that a track intervenes between the signal mast and the track to which the signal applies, e.g.: |
| double crossover | dvojitá koľajová spojka | N. Am.: Two crossovers, of opposite configuration, whose diverging routes cross in the middle. British: 'scissors crossover'. |
| double track line | dvojkoľajová trať |  |
| double-slip switch |  | A complex piece of trackwork with 2 entrances and 2 exits. A train entering at either entrance may be shunted to either of the 2 exits. Used sparingly due to high maintenance costs -- generally only in busy terminals where space is a premium. Double-slip switches have a relatively acute angle, #8 or #10. Some have 4 frogs (N. Am.), others have only 2 frogs and movable points. |
| dummy |  | British: a ground disc or shunting arm. |
| dwarf signal, low signal | trpasličie návestidlo | A signal, usually proportioned smaller than a high signal, mounted low, on the ground or just above it. Usually intended for use in low-speed areas such as terminal trackage, for trains travelling against the current of traffic, etc. Dwarf signals aspects may or may not match high signal aspects of the same name. On some railroads, dwarf signals can only display the lowest-speed aspects; on others, they can display a much wider range. |
| exchange station | výhybňa |  |
| face |  | A portion of a signal head, larger than the light-producing area (lens, etc.), which serves as a background and to blot out other potential interfering light sources, whether natural or artificial. Signal faces are almost invariably flat pieces of metal; may be round or square; are typically painted a dark color, frequently black; in Europe may be outlined but in America nearly invariably are not. |
| facing | nájazd z čela nábežnej koľajnice | Adjective indicating that the train is approaching the sharp ends of the points. In N. Am., the usage "facing-point switch" is often seen; in Britain, "facing points". Similar usage, in N. Am. and Britain, for crossovers. |
| feather |  | British: Slang for 'junction indicator'. |
| fish plate | koľajnicová spojka | A metal bar with holes, used to join the ends of 2 pieces of rail. |
| flangeway | okolkový žliabok | The channels within a frog (N. Am.) that allow the wheel flange to pass. |
| freight transport | nákladná doprava |  |
| frog | srdcovka, výhybka na troleji | N. Am.: The assembly of a switch where the two rails cross over each other. British equivalent: 'crossing'. The angle of a frog is generally given as a "number", denoting the ratio of offset to run. A #10 frog (a slow speed frog for the prototype, but a very "long" or "shallow" frog for model use) causes the track to diverge 1 meter for each 10 meters of forward travel. Britain: The pointed end of a crossing. Synonym: nose. N. Am. equivalent: 'toe (of frog)'. |
| gauge | rozchod | The distance between the rail heads. |
| gross tonne kilometer | hrubotonkilometer |  |
| guard rail | vodiaca (prídržná) koľajnica | Two short rails, parallel to the stock rails, that help prevent derailing. Guard rails are typically placed at the point where the opposite wheel is going through frog. Some applications required longer (some nearly full-length) guard rails. British: 'check rail'. Term also used in other contexts, such as on a bridge. |
| head |  | For lighted signals, a term describing the apparatus consisting of signal face, bulbs, lenses, and enclosure. |
| high signal | stožiarové návestidlo | A full-sized signal, mounted high, on a mast, bracket post, or signal bridge. Use of high signals is reserved, on some railroads, for main tracks, or when the current of traffic is toward that signal. |
| hook locking device | hákový uzáver |  |
| chair | podkladnica, podložka | British: equivalent to American 'tie plate'. |
| check rail | vodiaca (prídržná) koľajnica | British: equivalent to N. Am. 'guard rail'. Term also used in other contexts, such as on a bridge. |
| check rail | prídržnica |  |
| check rail plate | podkladnica k prídržnici |  |
| infrastructure manager | prevádzkovateľ infraštruktúry |  |
| interchange | križovatka, prestupná stanica |  |
| interchange, flyower crossing | mimoúrovňová križovatka |  |
| intermodal transport | intermodálna preprava |  |
| junction | križovatka | N. Am.: general term for the location where two tracks, often of two different railroad companies, come near each other and typically either join or include an interchange track. Britain: particular junctions of tracks as follows: |
| junction indicator |  | British: a row of 5 white lights indicating a diverging route. |
| ladder [track] | kmeňová, matičná koľaj | A multiply branched track allowing train movement from one track to one of many tracks. Frequently found at the ends of yards or at both sides of large passenger stations. Ladder tracks are usually in a one-to-many arrangement; however, many-to-many arrangements exist as well. |
| ladder siding |  | British: equivalent to N. Am. 'ladder'. |
| land take | záber územia |  |
| level crossing | úrovňové kríženie |  |
| line |  | In North America, a route. In contrast to 'track', 'line' refers to one or more tracks in a logical group. 'Lines' are typically spoken of in terms of their endpoints or some intermediate points: "the line to Chicago"; "the line via Yazoo City". Generally, lines are formally named. A scheme used by some railroads names lines, in decreasing order of importance/traffic volume: "___ Main Line" (or "___ Line"), "Branch", "Secondary Track", "Industrial Track", "Running Track". Another scheme expands on the concept of Division, naming each line "___ Subdivision". In Britain, 'line' is used both for a specific track of a set and for the set as a whole. |
| loop | slučka | N. Am. and Britain: a track that comes back on itself, allowing a train to change its direction of travel. Probably the best known example is Sunnyside Yard. Britain, most commonly: a track that comes off the main track, parallels the main track, then rejoins it in the same direction, allowing trains to pass or cross (Br.). Specific uses may be specified, as in "platform loop", "goods loop". Occasionally applied to more unusual arrangements, e.g., long crossovers, long connections between lines crossing at 90 degrees. |
| loose rock | drobivá hornina |  |
| lot | Ucelená časť stavby (UČS) |  |
| main line | hlavná dráha | The principal lines (routes) of a given railroad company, or country's rail network. |
| main track | hlavná trať | The principal track for travel, of a given line. That is, branch lines, secondary lines, etc. generally have a designated 'main track'. (They may also have subsidiary tracks such as sidings, yard tracks, etc.) |
| marker |  | A subsidiary signal light, often with a smaller or no face, which modifies the "main" aspect. [How official is such usage?] Sometimes used for a single arm of a signal when that arm can only show one color. |
| marshalling yard | preväzovňa |  |
| movable tongues | pohyblivé jazyky |  |
| movable-frog switch |  | N. Am.: A switch with a movable, rather than fixed, frog. Years ago quite a (surprising) number were installed in many locations, even in small yards and the like. Abandoned, probably because of high maintenance. Used now mostly in very high speed trackwork, for frog numbers that would otherwise not allow continuous wheel-rail contact. |
| movable-point crossing | výhybková križovatka | A crossing (N. Am.) which is not solid, but rather, has moving points. |
| narrow gauge | úzky rozchod | Any gauge narrower than Standard Gauge. Common ones include 1 meter gauge; 3 foot gauge; 2.5 foot gauge. |
| Network Management Statement | Sieťové prehlásenie |  |
| nose (of crossing) |  | Britain: The pointed end of a crossing. Synonym: frog. N. Am. equivalent: 'toe (of frog)'. |
| open cut tunnelling | hĺbenie tunelu |  |
| overpass | nadjazd |  |
| Pandrol clip | spona Pandrol | pozri "clip" |
| passenger transport | osobná doprava |  |
| passing siding | predbiehacia koľaj, výhybňa | [N.Am.] A siding used for trains to meet or pass. |
| path | trasa |  |
| pedestal signal |  | A 2-unit signal usually mounted on a short pedestal, implemented only on the PRR, to provide high-signal indications with dwarf-style aspects. Usually used in locations with little room for a high signal. |
| pedestrian bridge | lávka pre peších |  |
| peg | rameno mechanického návestidla | British: slang for semaphore blade. |
| platform | nástupisko |  |
| platform subway | podchod |  |
| point | hrotnica, výmena | The tapered, mobile rail of a switch, nearly always found as a pair. |
| points | výhybka | N. Am: plural of 'point' (q.v.). Britain: in the plural, equivalent to the N. Am. meaning. Used as a singular noun or in a noun phrase ("a points"; "a pair of points"), refers to the entire assembly, i.e., equivalent to N. Am. 'switch'. At the signaling level, "points" refer to all the points that are controlled as a single control lever or electrical circuit; thus a crossover could form one points. The points (Br.) are differentiated by designating an "A end" and "B end", etc. |
| position-light signal |  | A signal which uses the configuration of 2 or more lights to provide indications (information, meaning), and for which color is without meaning. In N. Am., implemented on Pennsylvania, Lehigh Valley, and Norfolk & Western as main and dwarf signals; also implemented on Erie as train order signals. In Britain, implemented as shunt signals. |
| precast segment | prefabrikát |  |
| rail | koľajnica | 'Rail' is the steel member upon which the train wheels rest. Previously rails were wooden, or wood with metal strips. |
| rail bed | koľajisko |  |
| rail expansion joint | koľajové dilatačné zariadenie |  |
| rail fasteners | koľajnicové upevňovadlo |  |
| rail-born sub-urban transport | prímestská koľajová doprava |  |
| rapid speed change | rýchlostný skok |  |
| receiving yard | príjazdové koľajište |  |
| relocate | posunúť |  |
| retention device | záver |  |
| revetment wall | oporná stena |  |
| roller chair | vlečková stolička |  |
| scissors crossover | dvojitá koľajová spojka | British equivalent of N. Am. 'double crossover'. |
| self-compacting concrete | samozhutňovací betón |  |
| self-propelled train | samostatné hnacie dráhové vozidlo |  |
| semaphore signal | ramenové návestidlo | A signal which provides its indication by position of an arm. The end of the arm typically points to the right on railroads with right-hand operation; to the left on railroads with left-hand operation. Blade colors and blade shapes may or may not be significant. Night aspects are typically given by color of light, via roundels near the fulcrum of the arm. |
| side-strips | postranné pásy |  |
| siding | vlečka | N. Am.: any track of lower rank that comes off the main track. It may be double-ended (rejoin the main track) but does not have to. Usually runs approximately parallel to the main track (cf. 'spur'). Britain: a single-ended track of lower rank that comes off the main track, either parallel or not parallel to the main track. Much less commonly double-ended. Usually a location where trains are stored while out of use (or being cleaned, loaded, unloaded, etc.). Sidings at yards are often double-ended; a common layout consists of "reception sidings", "sorting sidings", and "departure sidings" in sequence. |
| signal | návestidlo |  |
| signal bridge | návestný mostík | A structure for mounting signals that spans one or more tracks. Signal bridges may be footed on both ends, or they may be 'cantilever signal bridges', footed only on one end. |
| single turnout | jednoduchá výhybka |  |
| single-slip switch | polovičná križovatková výhybka | Diamond with Single Slip. British: equivalent to N. Am. 'single-slip switch'. |
| slab track | panelová trať, koľajište na betónovej doske |  |
| sleeper | podval | British: equivalent to American 'crosstie'. |
| sliding chair | klzná stolička |  |
| slot, slotting | prideľovanie časových intervalov | A "slot", or "slotting", is an arrangement whereby two signalmen can control a signal independently (neither's lever affects the other), with the logic resolved at the signal itself. Signals: "High", "dwarf", and "pedestal" aren't used. "Ground signal" means a shunting signal, whether or not ground-mounted. A running signal at ground level is not a ground signal. "Co-acting signals" show the same aspect and are within a couple of metres track-direction of the main signal. "Repeaters" show a modified aspect, and are significantly in rear. Both forms are used to extend sighting in some way. A "distant" signal shows a summary of the signals ahead, and is *not* automatic; the signalman can set it to a more restrictive aspect than a repeater at the same location would have. |
| spike | hreb | Square steel rods, with a tapered end and off-set head, used for attaching the rail to the crosstie. |
| Spring-mass system | systém odpruženia trate Spring-mass |  |
| standard gauge | normálny rozchod | When used generally, 4 feet 8.5 inches (1435 mm). However, a given locale (country, etc.) may have its own standard, and thus its own understanding of "standard gauge". |
| stock rail | opornica, oporná koľaj | The outermost rails of a switch (N. Am.), the ones unbroken by gaps of any sort. Most frequently one is straight and one curved; both may be curved in some circumstances. |
| structure-born noise | hluk vedený konštrukciou |  |
| sub-ballast mat | izolačná rohož pod koľajovým lôžkom |  |
| superstructure | horná stavba |  |
| swing-nose points |  | British equivalent to N. Am. 'movable-frog switch'. |
| switch | výhybka | In America, pertains to the entire assembly that allows trains to move from one track to another. Equivalent to British 'points'. |
| switch and crossing work |  | Britain: general term for the various ways that tracks intersect each other and trains are routed around junctions. |
| switch diamond | hrot srdcovky | British: equivalent to N. Am. 'movable-point crossing'. |
| switch rail | jazyková koľajnica |  |
| switch rail position limiter | obmedzovač polohy jazyka |  |
| temporary solution | provizórne riešenie |  |
| theatre indicator |  | British: a signal showing a number or letter when illuminated, indicating a route. |
| third party operator | tretí dopravca |  |
| thrusting roller chair | valčeková stolička dotlačovacia |  |
| tie | podval | N. Am.: Short for 'crosstie'. |
| tie plate | podkladnica, podložka | N. Am.: A metal plate placed between the rail and crosstie, more widely to distribute the load (car weight) from the rail to the crosstie. |
| toe (of frog) | hrot srdcovky | N. Am.: The pointed end of a frog. |
| track | trať, koľaj | Track' refers to the collection of structures upon which the train travels directly. Very generally, this means the rails, crossties (sleepers), and maybe ballast. In other words, the infrastructure. In North America, 'track' also has a more general meaning: the entire length of the infrastructure as an entity, e.g.: "the eastbound track", "track no. 1", "no. 1 track". British equivalent: 'line'. |
| track kilometer | železničný kilometer |  |
| track laying | pokládka koľají |  |
| traffic capacity | priechodnosť |  |
| trailing | nájazd z | Adjective indicating that the train is approaching from the frog (N. Am.) end. |
| train formation | vlakotvorba |  |
| train-kilometer | vlakokilometer |  |
| transhipment | prekládka |  |
| transhipment centre | prekladisko |  |
| transit route | prepravný koridor |  |
| transition rail | prechodová koľajnica |  |
| trough | žľab |  |
| truss | priehradový nosník |  |
| truss post | zvislica (priehradového nosníku) |  |
| truss, beam, support | nosník |  |
| turnout | výhybka, výhybňa |  |
| turnout | výmena | Britain: a track configuration where one track joins into another: |
| turntable | točnica |  |
| turntable with a guide disc | točnica s vodiacim kruhom |  |
| turntable with guide bars | točnica s vodiacimi lištami |  |
| wing rails | krídlové koľajnice | Two small rails, at the heel (N. Am.) end of the frog (N. Am.), parallel to the wheel path along the frog, that help prevent derailing. |
| wye | ypsilón | N. Am.: Literally, track arranged in the form of a letter "Y" with the endpoints joined. In some locations the trackage simply lends itself to such an arrangement. In others, one end of the wye is a stub-end track of limited length used for turning locomotives with or without cars. |
| wye track |  | N. Am.: For 2 tracks that are far from parallel and either cross, at grade or not, a track that joins the two tracks by curving from one to the other. Named because of its resemblance to one leg of a wye (N. Am., q.v.). If 2 such wye tracks exist, not in diagonally opposite quadrants, locomotives or trains can be turned to face the opposite direction. |
| yard | dvor |  |